## Slide 1: H410 Series Setup Transfer Tool manual

## Slide 2: Contents
Notes
Preparation - PC network settings (IP address)
Preparation - 410 Series System Settings (IP Address)
How to start Tool
Tool screen description
Tool operation instructions - Add Device
Tool operating instructions - delete device
Tool operating instructions - device connection
Tool operating instructions - reconnect device
Tool operating instructions - download configuration file
Tool operating instructions - upload configuration file
Tool operating instructions - Firmware Update

## Slide 3: Notes
The setting tool not usable during H410 series measurement. Please use after moving to the setting screen

## Slide 4: Preparation-PC network settings (IP address)
To establish the connection between the PC and the H410 series, set the network settings (IP address) on the PC side. (* Supported OS: Windows10)
Ethernet cable
Monitor cable
When hardware connection is complete, go to Control Panel> Network and Internet> Network and Sharing Center
Press "Ethernet"
②
Network settings
①

## Slide 5: Preparation-PC network settings (IP address)
①
②
③
Click "Properties"
Make sure that "Internet Protocol Version 4 (TCP / IPv4)" is checked and selected
Click "Properties(R)"

## Slide 6: Preparation-PC network settings (IP address)
①
④
Check "Use the following IP address (S)"
Enter "IP address (I)", "Subnet mask (U)", and "Default gateway (D)" referring to above [Setting example]
Check "Use the following DNS server address (E)"
No need to enter "Priority DNS server (P)" and "Alternative DNS server (A)"
Click "OK" to complete the IP address setting
②
③
⑤
[Setting Example]
IP Address(I)： 192.168.0.99
Subnet mask(U)： 255.255.255.0
Default gateway (D)：Blank

## Slide 7: Preparation --H410 Series System Settings (IP Address)
In order to establish the connection between the PC and the H410 series, configure the Ethernet settings (IP address) on the H410 series side.
Ethernet cable
Monitor cable
After starting the H410 series, touch "Settings" on the measurement screen
Ethernet settings
①

## Slide 8
①
②
Touch the tab “system settings”
Enter the Ethernet "IP Address", "Subnet Mask", and "Default Gateway" by referring to the [Setting example] below
Touch "Save" to complete the IP address setting
[Setting sample]
IP Address ： 192.168.0.100
Subnet Mask ： 255.255.255.0
Default Gateway ： 0.0.0.0
※If the value is not duplicated with the IP address on the PC side (example: 192.168.0.99) set in the previous section, it can be set in the range of 192.168.0.xxx (xxx = 1 to 254).
③
Preparation --H410 Series System Settings (IP Address)

## Slide 9: How to start Tool
Unfreeze “SetupTransferTool_Ver.xxx.zip”
Open “Release_Ver.xxx”
Tool will start when “SettingTool.exe” is double clicked
①
②
③

## Slide 10: Tool screen description
①
②
③
④
⑤
⑥
⑨
⑦
⑧

## Slide 11: Tool screen description
Device List
IP address
Add button
Remove button
Device Info
LAC Settings
Download Settings button
Upload Settings button
Firmware Update button
： Lists each device by IP address.
： The IP address added in ③ is displayed
： Add an IP address
： Delete the added IP address
： Displays the device information of the selected device
： Displays the "setting file" name on the H410 series
： Download the setting file on the H410 series
： Upload the setting file on the H410 series
： Update the H410 series IPU firmware

## Slide 12: Tool Operation Instructions-Add Device
①
②
③
Press “Add” button
Enter the IP address set in the previous section "Preparation H410 Series System Settings (IP Address)" and click the "OK" button
The IP address added to the "Device List" is displayed

## Slide 13: Tool operating instructions – delete device
①
②
③
Choose “Device List” and push “Remove” button
Press “OK” button
The IP address selected from the "Device List" will be deleted

## Slide 14: Tool operating instructions – device connection
①
②
③
To connect to the device and start communication, select the IP address in the "Device List"
After connecting the device, if communication starts normally, the information will be updated in "Device Info" and "LAC Settings"
If the device is not connected, "Disconnected" is displayed in "Device Info"
Device connecting screen
Device unconnected screen

## Slide 15: Tool operating instructions – reconnect device
①
If you want to reconnect the device or update the information in "Device Info" and "LAC Settings", select the IP address in "Device List" again

## Slide 16: Tool operating instructions-download configuration file
To download the setting file set in the H410 series, click the "Download Settings" button.
Set the file name with any name and click the "Save (S)" button to save the file in the folder * with the .lac extension
※ A folder is automatically created with the name of the connected Device List
①
②

## Slide 17: Tool operating instructions-upload configuration file
①
To upload the setting file to the H410 series, click the "Upload Settings" button
Select the .lac extension → click the "Open (O)" button
will be asked if you want to overwrite the system settings at the same time ※, so check it if you want to overwrite it
By clicking the "OK" button, the setting file will be uploaded to the H410 series
※Other than network related settings (IP address, netmask,gateway)
②
③
④

## Slide 18: Tool Operating Instructions-Firmware Update
①
To update the H410 series IPU firmware, click the "Firmware Update" button
Select the .dat extension for firmware update prepared in advance → Click the "Open (O)" button
A confirmation screen will be displayed. Click the "OK" button to start the firmware update
When the restart request screen is displayed, click the "OK" button and then restart the H410 series to complete the firmware update
②
③
④